Ellipse
An ellipse is a flattened circle, a plane curve, which results from the intersection of a cone by a plane in a way that produces a closed curve. It has two points called foci. It’s defined as the set of all points in a plane such that the sum of the distances from two fixed points (called foci) to each point on the ellipse is constant. we can also state that an ellipse is the image of a circle under parallel or perspective projection.

---
Scan converting an Ellipse
The ellipse is also a symmetric figure like a circle but is four-way symmetry rather than eight-way.

---
Polynomial method of defining an Ellipse
The ellipse has a major and minor axis. If a1 and b1are major and minor axis respectively. The centre of ellipse is (i, j). The value of x will be incremented from i to a1and value of y will be calculated using the following formula

---
Trigonometric method of defining and Ellipse
- x = a * cos (θ) +h and
- y = b * sin (θ)+k
- where (x, y) = the current coordinates
- a = length of major axis
- b = length of minor axis
- θ= current angle
- (h, k) = ellipse center
- In this method, the value of θ is varied from 0 to  radians. The remaining points are found by symmetry.

---
Midpoint Ellipse Algorithm
This is an incremental method for scan converting an ellipse that is centered at the origin in standard position i.e., with the major and minor axis parallel to coordinate system axis. It is very similar to the midpoint circle algorithm. Because of the four-way symmetry property we need to consider the entire elliptical curve in the first quadrant.

---
Let's first rewrite the ellipse equation and define the function f that can be used to decide if the midpoint between two candidate pixels is inside or outside the ellipse: